## Slide 1
G-2 tracker test beam T1042
Sergio Daniel Hernández Charpak – Universidad de Los Andes
Mentored by Brendan C Casey – Fermi National Laboratory
August 2015
The Muon
Same charge as the electron
200 times heavier More sensitive to new physics
Intrinsic magnetic moment, g Information about
Dirac predicted But experiment has differ.
Corrections with the Standard Model
Anomalous magnetic moment
Standard Model prediction:
Tracker
Straw trackers measure the beam profile as a function of time
3 stations located at 15°, 180° and 270° from injection point.
8 modules per station.
1 module 4 layers of straws
1 layer 32 straws wide
U V layers
Straw parameters | 
Wall Material | Aluminized Mylar
Wall thickness | 15
Wire Material | Gold plated Tungsten
Wire diameter | 25
Straw length | 10 cm
Stereo angle | from vertical
Operating Voltage | 1800 V
Straw parameters | 
Wall Material | Aluminized Mylar
Wall thickness | 
Wire Material | Gold plated Tungsten
Wire diameter | 
Straw length | 10 cm
Stereo angle | 
Operating Voltage | 1800 V
Test Beam June 2015
Motion table
FLOBBER cooling
Vacuum chamber
MWPC
Silicon
Tracker
FLOBBER
MTest (FNAL)
2 weeks
120 GeV protons
Tracker module
Ar-CO2 & Ar-Ethane
High Voltage
Iseg EHS 8220p-F
Switched Mode Power Supply (Supply)
Low ripple and noise
Resolution few pA
Remotely controllable via SNMP
Friendly GUI
Operated at 1400-1500-1600-1700-1800 V
Ramp speed of 5%
Current trip of 20
Test Beam Data Analysis
Existing gm2 simulation and analysis software (Geant4/Art, C++, Root)
Straw digits hits per layer
Time Differences between hits by layer
Hits which are less than 500 ns apart
Looping for hits in 4 layers
Results
Hits are correct.
Gaussian and flat noise fit
Most are beneath the Gaussian.
Higher Threshold – Less noise
Differences between gas unclear
Still more analysis to do looking more into detail in all the parameters.
*Readout Electronics Threshold
Abstract
The Muon g-2 experiment is on the frontier of Particle Physics. Its tracker system is based on Straw Detectors. A prototype of these has been successfully tested in Fermilab’s Mtest Facility during June 2015. During this test, a High Voltage (HV) supply powered the straws and was operated at different voltages. During the offline analysis of this data, variation of parameters as Threshold, HV, beam rate and type of gas were subject of study. An inverse proportion relation was found between threshold and noise (higher threshold, lower noise) but more detailed analysis is needed for more conclusive results.
Muon G-2
G-2 aims to measure of the muon with better precision (140 ppb) than the previous Brookhaven’s E821 (0.7ppb)
Big Collaboration
Get clues about physics Beyond the Standard Model.
Conclusions
Experiment in the frontier of the Standard Model
Test beam was an opportunity to see collaboration happen
Operated the HV module and gained knowledge about it.
Run 413 – Threshold* 1000mV – HV 1800 V – Beam Rate 100k
Run 405 – Threshold* 400mV – HV 1800 V – Beam Rate 100k
Run 340 – Threshold* 1200mV – HV 1600 V – Beam Rate 10k
Run 314 – Threshold* 300mV – HV 1500 V – Beam Rate 10k
Argon:Ethane (50:50)
Argon:Co2 (80:20)
The time differences between straw layers . The hits registered by the straws represent the reality.
The higher threshold, the less noise.
There is still analysis to be done.
References
"Muon G – 2 Technical Design Report." Fermi National Accelerator Laboratory, 15 June 2015. Web. 26 June 2015.
Li, Liang. "Muon G-2 Experiment at Fermilab." Shanghai Jiao Tong University, 5 June 2013. Web. 15 June 2015.
32 straws long
u1
u2
v1
v2
Image 2 - Straw tracker – Summer 2015
Image 1 – G-2 Collaboration in the storage ring – July 2015
Table 1 – Straw Parameters
Image 3 – Test Beam June-July 2015
Image 4 – Test Beam Team June 2015
Image 5 – HV plugged in
Image 6 – Iseg SNMP GUI
Image 7 – Straw UV 4 layers
Acknowledgments
Brendan C Casey – Fermi National Laboratory
Thomas Stuttard – University College of London
Tammy Walton – Fermi National Laboratory
Brendan Kiburg - Fermi National Laboratory